The Bootleg Sixties Show

Technical Rider and show info as of 19th February 2020

Page 1 of 4

Show Description

The show has 1 x LCD beamer on a 1 metre Unicol drop pole with a total flown weight of 35K, flown from a downstage bar ( see attached hanging plot sheet) This projects onto a rear flown white gauze.

We require a projection distance of 6.5m from the beamer to the gauze

Lights

We require 5 mid- stage LX  bars ;

LX 1, 3 and 5 for your lights

LX 2 and 4 for our touring moving lights

Please send us a plan showing your lighting bars and voordoek, and a list of the available lights you have. We will inform you of the lighting gels we need and where the colours will go. Please have your lights pre-rigged before our arrival. We need you to supply 48 CP62 par cans, spread over 3 lighting bars ( 16 per bar ) as follows :

LX 1 : 16 x par cans

LX 2 : Our touring moving lights

LX 3 : 16 x par cans

LX 4 :  Our touring moving lights

LX 5 : 16 x par cans

We also require 4 x PCs of yours on the portal to focus on our backline and  6 x specials on your front truss to focus on the front musicians.

The Show

The stage is then set up as for a regular band lineup.

We project videos behind the band throughout the show

We would also like to use strobe effect lighting, haze, smoke and streamer cannons

Streamer Cannons

WE WOULD LIKE TO FIRE 2 STREAMER CANNONS. THESE ARE POWERED BY COMPRESSED AIR (NOT PYROTECHNIC)

(PLEASE NOTE…THEY ARE STREAMERS,  NOT CONFETTI)

We would need a FOH control area (6 seats wide 2 seats deep)

for sound & lighting desk

We will control onstage monitors & AV from stage left

Page 2

The Cast ( Band ) is made up of 5 male singers / musicians

We will be travelling with 5 crew :

Foh Engineer / Production Manager

Stage Manager / AV Operator

Lighting Engineer

Monitor Engineer

Backline technician

Technical & Staging

We require you to supply 7 x  risers

3 x 1x 2 metre units at 40 cm high for drums ( centre stage )

4 x 1 x 2 metre x 20 cm high for keyboards ( stage left and stage right )

We will require black valance to cover the front of all three risers

The stage / performing area to be covered with black Marley flooring

We rquire stage size to be 11metres wide

We require you to supply 4 talk back /comms headsets :

2 stage left,  2 front of house

Sound

We require you to supply a quality full range auditorium speaker system producing full range 20 - 20k, capable of producing 95db at your FOH position

Can you  please provide 4 wedges & amps

2 x to be used as side fills  (in stereo please ) on stands if required

The send to these will be from the monitor board at stage left

2 x to be put at the corners of the stage as audience fills. These can be in mono.

All sends to Main sound system and front audience fills need to be from FOH position

We will supply FOH & Monitor desks, mics, leads, mic stands, and all backline and instruments for the show. We have the facility to connect our FOH  desk with rj45 (supplied)

We will be using 3 Radio packs ( for vocals) 3 radio packs ( for guitars )

Frequencies from :

830.100

830.500

830.900

831.300

831.900

Page 3

We will also be using 5 In - Ear Monitoring systems

Frequencies from :

863.250         863.100

863.740         863.900

864.625         864.500

864.990         864.900

Power

We require 3Phase 32-amp supply ( at stage left please )

Dressing Rooms

4 rooms are required, please

3 rooms for the artist

1 room on stage level for production

Get In

Load – in time is 1.00 pm ( 13.00 )

Please note we need 4 stage hands for the get in, then 4 for the get out.

IT IS CRUCIAL TO THE SHOW THAT THESE STAGE HANDS ASSIST US WITH DE-RIGGING AND LOADING OUT OUR EQUIPMENT BEFORE THEY DE-RIG ANY HOUSE EQUIPMENT. IF THIS IS NOT POSSIBLE, THEN 2 SEPARATE STAGEHANDS NEED TO BE PROVIDED TO HELP US. WE MUST NOT BE LEFT TO LOAD THE VANS ALONE

During the build we need a flyman, lighting man & sound tech

Build time for the show is approx.. 4 hours

WE HAVE GIVEN YOU TIMINGS FOR AN 8pm SHOW. IF THE SHOW IS AT ANY OTHER TIME WE WILL CONTACT YOU AND CHANGE THE ARRANGEMENTS ACCORDINGLY

Daily production schedule would therefore be :

1 pm – 4pm get in and build

2 pm  - backline and band arrive

5.30 pm – 6.30pm sound check

Then final focus / stage blackout until till doors open

The show runs :

60 minutes first half

60 minutes second half

Merchandise

We will sell merchandise before and after the show

We would like an area a minimum of 3m wide, with adequate lighting and mains electricity within 3m of the selling position.

We will also need a selling table.

Page 4

Parking

We will travel in :	 1 x Mercedes jumbo Sprinter van

1 x Mercedes standard length Sprinter van

1 x Peugeot Boxer LWB van

Contacts

Production Manager

Arthur Anderson

Mb 0044 (0) 7885 162122

Email:      arthur@thebootlegsixties.com

Website      www.thebootlegsixties.com

Stage Manager

Tony Henderson

Mb 0044 (0) 7885 093379

Email :      tony@thebootlegsixties.com